## Slide 1
Why Key Space Matters
Featuring 35 Historic Cipher Machines
Copyright © 2023
CC Attribution 4.0 International
Ralph Simpson
Ralph@CipherHistory.com
February 19, 2023
Ralph Simpson
Proprietor & Curator
Notes: Ralph Simpson Bio
Ralph Simpson worked in the computer industry for 32 years, working for IBM and Cisco Systems. He started as a systems engineer for large mainframe computers and held a variety of technical and management roles, including authoring an IBM Technical Manual on redundant systems. He retired as Senior Director for Service Strategy at Cisco Systems, with responsibility for 2,500 engineers.
Ralph is now retired and volunteers at History San Jose and the Computer History Museum. He wrote a book on cipher history called, Crypto Wars: 2000 Years of Cipher Evolution. He is also an avid collector of cipher machines, which you can see on his website, CipherHistory.com. Ralph lives in San Jose in a restored Victorian house, which is home to his Cipher History Museum and a very understanding wife.

## Slide 2: 35 Historic Ciphers... and 4 Modern Ones
Cipher
Year
Monoalphabetic
Caesar
Vigenère (repeating key)
Vigenère (autokey)
Playfair
Wheatstone Cryptograph
Lugagne Transpositeur
M-94 Cylinder Cipher
M-138A Strip Cipher
ADFGX / ADFGVX
Hebern 5-Rotor
Kryha
Enigma Swiss K
Lugagne Le Sphinx
Abwehr Enigma G
Enigma I
SIGABA
Japanese Purple
600 BCE
50 BCE
1466
1586
1854
1860s
1912
1912
1916
1918
1922
1924
1926
1930
1931
1932
1937
1939
Cipher
Year
Japanese JN-25 Codebook
Lorenz SZ-40/42
SG-41 “Hitler Mill”
M-209 Pin & Lug
Enigma M4
T-52d Geheimschreiber
Typex Mark 22
NEMA
Hagelin C-52 / CX-52
KL-7
Transvertex HC-9
VIC Pencil & Paper
Hagelin CD-55 / CD-57
Fialka
DES (56 bit)
RSA-4096
AT&T 3600E Clipper Chip
AES-256
1939
1941
1941
1942
1942
1942
1943
1947
1952
1952
1950s
1953
1955/7
1956
1976
1977
1992
2001
Copyright © 2023 ( CC BY 4.0 ) CipherHistory.com
Notes: So, why does key space matter? An understanding of key space unlocks a deeper understanding of how a cipher machine works. The key space of a cipher machine even gives an insight into the mind of the inventor, codebreaker, and user. Knowing the tradeoffs between ease-of-use, cryptologic strength, manufacturing complexity, user errors, etc. tells us why specific decisions were made in the design and use of the cipher machine.
To attain this level of understanding of each cipher machine, the theoretical "Maximum key space" will be compared to the "Practical key space". The practical key space is the final cryptosystem as viewed and attacked by the enemy cryptanalyst. The ability to compare, contrast, and analyze the differences between the maximum key space and the practical key space provides a new way to study the relative effectiveness of the machines in theoretical and real-life situations.
Each historic cipher machine will be deconstructed to show the contribution to the key space of each component. The calculation of the practical key space will assume the codebreaker has the enemy cipher machine and knows exactly how it was used, including any self-imposed and situational limitations. The only unknown is the key itself.
There are several surprises in this list, not only in terms of the size of the key space, but also in terms of why some decisions were made in the design or usage of the cipher machines. Some of the decisions show a surprising lack of cryptologic knowledge or appreciation for the skills of the enemy cryptanalysts.
Why Key Space Matters
Key space is an important but elusive concept in cryptology. It primarily relates to the number of settings that need to be tested to break a cipher system by brute force. While this is a reasonable measure of cryptologic strength for the latest cryptologic systems like AES and RSA, it is less reliable but still important for historic cipher systems.
Key space is an elusive concept because wildly different key spaces are often reported for the same device. Each of these various key spaces could be valid, but may have been based on different assumptions which are not always explicitly stated. This presentation will clearly state the assumptions and apply them precisely to each device.
But the size of a key space can be a misleading measure of cryptologic strength, particularly for historic cipher devices, because techniques have been developed to speed and enhance codebreaking without the need to use brute force.

## Slide 3: What is a Key vs. Key Space?
Key is the set of information needed to apply to a cryptosystem in order to encrypt or decrypt a message
  Modern keys are passwords, pin #s, fingerprints, etc.
  Historic keys are usually machine settings; such as rotor settings, plugboard connections, etc.
Key Space is the sum of all possible keys of a cryptosystem which are valid and unique

## Slide 4: Why Key Space Matters
  But, key space matters because it is a pathway to:
    Unlock the mystery of how a cipher machine works
    Understand the cryptologic tradeoffs in design & use
    Enter the mind of the inventor, codebreaker, and user
Caution!
​Key space allows easy comparisons of cryptologic strength between cipher systems
But…
It only measures effort for brute force attacks,
and most historic ciphers can be broken by other means

## Slide 5: A Short Note about Scientific Notation
Scientific Notation:
  Shorthand for large numbers
  Easy way to compare order of magnitude differences
  Example: 1026 is…
  - 10 times larger than 1025
  - 1 million times larger than 1020
  Historic precedents for describing key space in cryptology:
    Historic devices use base 10 or powers of 10, ie. 10X
    Modern encryption use base 2 or # bits, ie. 2X
Cryptology commonly uses absurdly large numbers, some of the largest encountered in the natural world

## Slide 6: Assumptions about Key Spaces
Maximum key space:
  The base machine is captured and known to the enemy
  (per Kerckhoffs’s Principle)
  Field replaceable parts (ex. rotors, reflectors) are unknown
  “Message setting” is included in key space
Practical key space:
  Same as above, plus…
  Field replaceable parts are also known
  User imposed limitations are known and exploited
These assumptions are from the NSA pamphlet,
“The Cryptographic Mathematics of Enigma”
Notes: To use the Enigma machine as an example, the Maximum Key Space is:
    If the enemy captures an Enigma, then the base machine would reveal the wiring of the entry disk, which is not changeable in the field.
    Rotor and reflector wirings can be changed, so they are assumed to be unknown.
    Notch location can be changed, so it is unknown.
  The Practical Key Space is:
    The enemy has the reflector, so it adds no cryptologic strength.
    All 5 available rotors are captured, so wiring and notch location is known.
    Also known are user imposed limitations, such as, always using 10 plugboard cables, no rotor allowed in same position on subsequent day, no 3 rotor combination repeated within same month.
    Consecutive Stecker Knock Out was not included because it was only used by a few networks
    Even though a single message can be broken without knowing the message setting, other messages using the same internal setting cannot be broken. So, the NSA assumes that the message setting (the rotor start position) must be known so all the daily messages can be broken.
  NSA document, “The Cryptographic Mathematics of Enigma”: https://www.nsa.gov/portals/75/documents/about/cryptologic-heritage/historical-figures-publications/publications/wwii/CryptoMathEnigma_Miller.pdf

## Slide 7: Monoalphabetic Cipher Key Space
Monoalphabetic Cipher:
a substitution cipher where any letter can encrypt to any other letter, key space = 26!
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
p | c | r | l | j | s | g | u | a | v | b | f | x | y | i | m | w | d | h | t | e | o | k | z | n | q
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
d | e | f | g | h | i | j | k | l | m | n | o | p | q | r | s | t | u | v | w | x | y | z | a | b | c
Caesar Cipher:
the simplest monoalphabetic cipher, shift of alphabet from 1 to 25 positions
Maximum & Practical key space
25
Maximum & Practical key space
4.03 x 1026

## Slide 8: Vigenère Disk Example Key Spaces
Repeating keyword
key space = 26(keyword length)
Example: keyword is
“Manchester Bluff” - 2615
Autokey or book cipher*
key space = 26(message length)
Example: message is
314 characters - 26314
Maximum & Practical key space
1.68 x 1021
Maximum & Practical key space
2.00 x 10444
* Autokey, invented by Vigenère, or a book
cipher means key is as long as the message
Photo credit: Stafford Museum, Stafford, VA

## Slide 9: Playfair Key Space
Maximum & Practical key space
6.20 x 1023
Playfair 5x5 matrix = 25!
(But for each matrix, shifting rows
or columns 1-5 places are equivalent)
25! / (5x5) = 24!
M | A | N | C | H
E | S | T | R | B
L | U | F | D | G
I/J | K | O | P | Q
V | W | X | Y | Z
H | M | A | N | C
B | E | S | T | R
G | L | U | F | D
Q | i/J | K | O | P
Z | V | W | X | Y
E | S | T | R | B
L | U | F | D | G
I/J | K | O | P | Q
V | W | X | Y | Z
M | A | N | C | H

## Slide 10: Wheatstone Cryptograph Key Space
Maximum & Practical key space
4.03 x 1026
Inner disk alphabet
is the key = 26!
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 11: Lugagne Transpositeur Maximum Key Space
Maximum key space
1.30 x 10532
20 strips: (26!)20 =
1.30x10532
Order: 1
10 pairs alphabet strips:
Offset fixed: 1
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 12: Lugagne Transpositeur Practical Key Space
Practical key space
1.32 x 1013
20 strips: 120
Order: (10!)2 =
1.32x1013
10 pairs alphabet strips:
Offset fixed: 1
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 13: M-94 Maximum Key Space
Maximum key space
3.45 x 10666
Mixed alphabet on disk:
(26!)25 = 1.38x10665
Row offset:
= 25
Disk order on spindle: = 1
Photo credit: Ralph Simpson, CipherHistory.com
Notes: All reporting I could find reports cylinder cipher key space without the row offset included. This begins with Thomas Jefferson, who claimed his 36 Wheel Cypher had a key space of 36!. This makes little difference, but should be included for accuracy.

## Slide 14: M-94 Practical Key Space
Practical key space
3.88 x 1026
Mixed alphabet
on disk: = 125
Row offset:
= 25
Disk order on spindle: = 25!
The key space for the cylinder cipher has been incorrectly reported as (#disks)! since its invention by Thomas Jefferson, which ignores the row offset
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 15: M-138A Maximum Key Space
Maximum key space
3.69 x 10799
30 Strips:
30 mixed strips:
(26!)30 = 1.47x10798
Order: 1
Offset: 25
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD
Notes: The M-138A actually had 100 alphabet strips, each with a different mixed alphabet. Since the alphabet on all 30 strips used for the calculation are unknown, having more than 30 strips does not add any key space.

## Slide 16: M-138A Practical Key Space
Practical key space
1.95 x 1059
30 Strips from 100:
30 mixed strips: 1
C(100,30) = 2.94x1025
Order: 30!
Offset: 25
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD
Notes: C(100,30) X (order of 30!) is the same as P(100,30), but I wanted to specifically highlight the two contributors to key space being the selection of 30 alphabetic strips from a group of 100, and then the order of those strips in the device.

## Slide 17: ADFGX Cipher Key Space
Maximum & Practical key space
4.19 x 1047
5x5 Substitution table:
= 25! = 1.55x1025
8 | 12 | 2 | 10 | 9 | 1 | 15 | 7 | 16 | 6 | 14 | 5 | 3 | 13 | 4 | 11
D | X | D | F | A | G | A | D | D | G | F | F | X | A | A | X
A | F | X | D | D | F | G | G | X | F | G | A | D | D | X | D
F | X | F | G | G | D | X | A | A | X | A | D | G | G | F | X
A | D | A | G | A | X | D | X | A | F | X | G | F |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
G | D | X | A | F | G | D | D | A | F | X | X | A | F | A | D
F | X | D | X | A | F | G | A | D | D | D | F | D | G | G | X
D | F | G | F | D | X | A | F | G | G | X | X | G | A | X | A
X | A | F |  | G | F | X | A | A | G |  | D |  | X | D | A
Transposition 16-23 columns:
∑ n! = 2.70x1022
n=16
23
 | A | D | F | G | X
A | G | H | Q | F | L
D | Z | K | T | X | M
F | O | W | S | A | C
G | I | D | N | P | U
X | E | V | B | Y | R
Notes: Examples of ADFGX messages used by the Germans in WW1 included transpositions between 16 and 23 columns, so that was used as the possible range for the transposition calculation,

## Slide 18: ADFGVX Cipher Key Space
Maximum & Practical key space
1.01 x 1064
 | A | D | F | G | V | X
A | G | 3 | Q | F | 6 | L
D | Z | K | 0 | X | M | T
F | O | 9 | J | A | C | 1
G | I | D | 8 | 5 | U | 4
V | E | V | B | Y | R | H
X | 4 | N | 7 | W | 2 | P
6x6 Substitution table:
= 36! = 3.72x1041
8 | 12 | 2 | 10 | 9 | 1 | 15 | 7 | 16 | 6 | 14 | 5 | 3 | 13 | 4 | 11
D | X | V | F | V | G | A | D | D | G | V | 3 | X | A | A | 2
A | F | X | V | 1 | 6 | G | G | X | 7 | G | A | D | D | X | D
9 | D | V | G | G | V | X | A | A | 2 | A | D | 4 | V | F | X
I | D | 8 | 5 | A | 4 | D | F | V | V | X | G | F |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
G | V | X | A | 3 | G | D | D | V | F | 2 | X | A | V | A | D
6 | X | D | X | A | 7 | G | A | 1 | V | D | F | D | G | G | X
V | V | 4 | F | D | 2 | A | 9 | G | G | X | D | V | A | X | A
4 | 8 | F |  | G | V | F | I | A | 5 |  | D |  | X | D | V
Transposition 16-23 columns:
∑ n! = 2.70x1022
n=16
23
Notes: This cipher was broken on the day it was first deployed by the Germans in early June, 1918 and continued to be broken until the end of WW1. It was broken by French Army Lt. Georges Painvin, who also broke the earlier ADFGX cipher.

## Slide 19: Hebern Maximum Key Space
Maximum key space
1.27 x 10140
Wiring: (26!)5 =
1.07x10133
Order: 1
Side: 1
Start position: 265
5 Rotors:
Photo credit: Smithsonian National Museum of American History, Washington, DC
Notes: Note that when using all possible wirings of the 5 rotors, a single message can be broken without knowing the start position.
The NSA document that calculates of the Enigma key space (see slide #6 notes) includes the rotor start position because that is needed to break any other messages sent with that same rotor order, which usually remains the same for each day.
The rotor start position is the message key, which would change with each message. So, rather than break the rotor wiring again, only the starting position of the rotors need to be determined for every messages sent with that rotor wiring configuration, so solving this once means all messages can be broken for that day.

## Slide 20: Hebern Practical Key Space
Practical key space
4.56 x 1010
Wiring: 15
Order: 5x4x3x2x1
= 120
Side: 25
Start position: 265
5 Rotors:
Photo credit: Smithsonian National Museum of American History, Washington, DC

## Slide 21: Key Spaces of Historic Cipher Machines
4.03x1026
2.50x101
1.68x1021
2.00x10444
6.20x1023
4.03x1026
1.30x10532
3.45x10666
3.69x10799
4.19x1047
1.01x1064
1.27x10140
4.03x1026
2.50x101
1.68x1021
2.00x10444
6.20x1023
4.03x1026
1.32x1013
3.88x1026
1.95x1059
4.19x1047
1.01x1064
4.56x1010
Monoalphabetic
Caesar
Vigenère (15 char. repeating key)
Vigenère (314 char. autokey)
Playfair
Wheatstone Cryptograph
Lugagne Transpositeur
M-94 Cylinder Cipher
M-138A Strip Cipher
ADFGX
ADFGVX
Hebern 5-Rotor
288
25
271
21476
279
288
21768
22214
22656
2158
2213
2466
288
25
271
21476
279
288
244
288
2197
2158
2213
235
600 BCE
50 BCE
1466
1586
1854
1860s
1912
1912
1916
1918
1918
1922
Maximum Key Space
Practical Key Space
Cipher
Year

## Slide 22: Kryha Maximum Key Space
(2617 x 26!) x (26 x 17) =
(4.57x1050) x (26 x 17)
Maximum key space
2.02 x 1053
Georg Hamel calculated the Kryha key space as 4.57x1050 and claimed only immortals could break it. William Friedman and others broke Khrya in 2 hours and 41 minutes…
Cipher rotor:
Mixed alphabet: 26!
Start position: 26
17 Segment wheel:
# patterns: 2617
Start position: 17
Historical Deduction
therefore, Friedman is immortal!
(2617 x 26!) x (26 x 17) =
(4.57x1050) x (26 x 17)
Photo credit: Invaluable Auctions
Notes: Later Kryha devices had more than 17 segment wheels, or multiple wheels. This particular early model is shown because this was the model Georg Hamel used to calculate key space.
Hamel’s calculation is correct, but does not include the starting positions of the 2 disk, which would be required knowledge to be able to break other messages sent with the same disk configuration. In other words, the starting positions of the two disks is sent as part of the “message key”.

## Slide 23: Kryha Practical Key Space
Practical key space
1.78 x 1029
Pin wheel (0-16 pins):
# wheels: 1
Start position: 17
Cipher rotor:
Mixed alphabet: 26!
Start position: 26
Photo credit: Invaluable Auctions

## Slide 24: Swiss K Enigma Maximum Key Space
Reflector:
Wiring: (26!)3
Order: 1
Ring setting: 262
Start position: 263
Maximum key space
1.60 x 10101
3 Rotors:
Wiring: 7.91x1012
Start position: 26
Photo credit: The Military Museums, Calgary, Alberta, Canada
Notes: Reflector looks like a 4th rotor, but the wiring is paired reciprocally. This means if A encodes to X, then X encodes to A. This reduces the key space, but allows encoding and decoding to operate identically without any change of machine settings, such as a code/decode switch as is used on the Hagelin pin&lug devices.
The difference in key space is reciprocal reflector = 7.91 x 1012 vs non-reciprocal reflector = 26! = 4.03 x 1026. This is a factor of 100,000,000,000,000 or 100 trillion times greater.

## Slide 25: Swiss K Enigma Practical Key Space
Reflector:
Wiring: 13
Order: 3x2x1= 6
Ring setting: 262
Start position: 263
Practical key space
1.85 x 109
3 Rotors:
Wiring: 1
Start position: 26
Photo credit: The Military Museums, Calgary, Alberta, Canada

## Slide 26: Lugagne Le Sphinx Maximum Key Space
Maximum key space
1.30 x 10532
20 strips: (26!)20 =
1.30x10532
Order: 1
20 interchangeable alphabet strips:
Offset fixed: 1
Photo credit: CryptoMuseum.com
Same key space as Transpositeur cipher
Notes: Cryptographically, the only difference in this Lugagne device from the first version, 18 years earlier, is the alphabet strips are now interchangeable from top and bottom. This means the Maximum key space remains the same as the earlier model, but the Practical key space improves significantly, from 1013 to 1024.

## Slide 27: Lugagne Le Sphinx Practical Key Space
Practical key space
2.43 x 1024
20 strips: (1)20
Order: 20! =
2.43x1024
20 interchangeable alphabet strips:
Offset fixed: 1
Photo credit: CryptoMuseum.com

## Slide 28: Abwehr Enigma G Maximum Key Space
Reflector:
Wiring: (26!)3
Order: 1
Notches: (226)3
Ring setting: 13
Start position: 263
Maximum key space
7.17 x 10121
3 Rotors:
Wiring: 7.91x1012
Start position: 26
Photo credit: Bletchley Park Trust
Notes: Note the Maximum key space is greater than the standard 3 rotor, plugboard Enigma of 10114. The Practical key space will be considerably lower. The big difference is the unknown number of notches on the rotors, which add no key space after the rotors are known.

## Slide 29: Abwehr Enigma G Practical Key Space
Photo credit: Bletchley Park Trust
Reflector:
Wiring: 13
Order: 3x2x1 = 6
Notches: 13
Ring setting: 263
Start position: 263
Practical key space
4.82 x 1010
3 Rotors:
Wiring: 1
Start position: 26

## Slide 30: Enigma I Maximum Key Space
Reflector:
(2p-1)(2p-3)…(1) = 7.91x1012
Plugboard 0-13 plugs:
∑ C(26,2p)x(2p-1)(2p-3)…(1) =
5.33x1014
Wiring: (26!)3
Order: 1
Ring setting: 262
Start position: 263
Maximum key space
3.28 x 10114
3 Rotors:
p=0
13
Photo credit: Ralph Simpson, CipherHistory.com
Notes: Plugboard setting:
    Since any number of plugs from p=0 to p=13 can be used, the formula is:
    The reflector and plugboard are both reciprocal, and the reflector swaps all letters, so it uses the same formula as above with p=13.
    This calculation is the same as the NSA document, “The Cryptographic Mathematics of Enigma” by Dr. Ray Miller.
    All possible wirings are used for the 3 rotors, so a single message can be decrypted without knowing the start position. To decrypt all the messages using the same daily setting, then the start position must be known.
    The entry disk is not considered in the key space because it is hardwired to the plugboard and cannot be re-wired in the field.
∑ C(26,2p)x(2p-1)(2p-3)…(1) = (26!/(26-2p)!(2p)!) x ((2p)!/(p!)(2p)
= 26! / ((26-2p)!(2p)!)(p!)(2p)
= 5.33x1014
p=0
13

## Slide 31: Enigma I Practical Key Space
5x4x3 = 60
Reflector: 1
1.51x1014
Wiring: 13
Order:
Ring setting: 262
Start position: 263
1.07 x 1023
3 Rotors from 5
In mid-1940, Germany changed 2 procedures:
NO ROTOR IN SAME POSITION from previous day, rotor settings reduce from 60 to 32 daily
NO 3-ROTOR COMBINATION REUSED in same month; settings reduce from 60 to 30, or 50%
1&2 above: (32+16)/2=24 avg. rotor orders
Practical key space
4.31 x 1022
avg. 24
Plugboard - 10 cables:
Photo credit: Ralph Simpson, CipherHistory.com
Notes: No rotor in same position from previous day, if rotor order I,II,III was used on one day, then the next day the following rotor configurations would not be allowed:
    All combinations with rotor I in first position:
    = 4x3 combinations = 12
    [All combinations with rotor II in second position] – [combinations with rotor I in first position or rotor III in third position (already counted above)]:
    = 4x3 combinations – (I,II, IV or V) – (IV or V,II,III) = 12 – 2 – 2 = 8
    [All combinations with rotor III in third position] – [combinations with rotor I in first position or rotor II in second position]:
    = 4x3 combinations – (I, IV or V, III) – (IV or V, II, III) = 12 – 2 – 2 = 8
    Total = 12 + 8 + 8 = 28 rotor combinations would not be allowed
    Total rotor combinations allowed = (5x4x3) – 28 = 32
No 3 rotor combination allowed in the same month. Each 3 rotor combination has odds 5x4x3 = 60, so over a typical 30 day month, the odds of any combination reduces from 60 down to 30 over the month.
Combining the two items above means 32 possible 3 rotor positions on the first day of the month reduces to 32 X (30/60) = 16 possible rotor positions on the last day of a 30 day month, so on average, there are (32 + 16) / 2 = 24 possible 3 rotor positions to check.
Note that the plugboard could have been made non-reciprocal, but a key space of 1014 was considered sufficient. The non-reciprocal plugboard was tested but viewed as too complex and error-prone for the operators for the improvement in key space to 1024. Because the plugboard was separated from the rotors cryptographically by Marian Rejewski, this difference became a moot point since both reciprocal and non-reciprocal plugboards could be easily broken after the rotors were deteremined.
CSKO Odds - Consecutive stecker knock out rule: adjacent letters of the alphabet are not steckered (ex. B could not be steckered to A or C). This was used by the Luftwaffe, but was not used for the Army or Navy, so was excluded from the key space calculation.

## Slide 32: SIGABA Maximum Key Space
Wiring: (26!)10
Order: 1
Side: 1
Start position: 2610
5 Index rotors:
Wiring: (10!)5
Order: 15
Side: 15
Start position: 105
Maximum key space
1.82 x 10285
Index rotor logic:
10! / 25 = 1.13x105
10 Cipher /
control rotors
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD

## Slide 33: SIGABA Practical Key Space
Wiring: 110
Order: 10!
Side: 210
Start position: 2610
Practical key space
5.95 x 1028
10 Cipher /
control rotors
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD
5 Index rotors:
Wiring: 15
Order: 5!
Side: 15
Start position: 105
Index rotor logic:
10! / 25 = 1.13x105

## Slide 34: Japanese Purple Cipher Maximum Key Space
Wiring: 13
Order: 3x2x1 = 6
(fast, med., slow)
Start position: 253
Three - 20s
stepping
switches:
Wiring: 1
Order: 1
Start position:
= 25
One - 6s
stepping
switch:
Output
plugboard:
Maximum key space
3.81 x 1059
(26!)(6x253)(25)(26!) =
Input plugboard:
20 consonants
6 vowels
Non-reciprocal: 26!
20 consonants
6 vowels
Non-reciprocal: 26!
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD

## Slide 35: Japanese Purple Cipher Practical Key Space
Practical key space
1.45 x 1031
(26!)(6x240)(25)(1) =
User restriction: Initally 120 start positions were used, by 5/1/1942, 240 were used
Wiring: 13
Order: 3x2x1 = 6
(fast, med., slow)
Start position: 253
Three - 20s
stepping
switches:
Wiring: 1
Order: 1
Start position:
= 25
One - 6s
stepping
switch:
Output
plugboard:
Input plugboard:
20 consonants
6 vowels
Non-reciprocal: 26!
20 consonants
6 vowels
Non-reciprocal: 26!
User restriction: Input and output plugboards are set identically; 2nd plugboard: 1
= 240
1
Photo credit: Ralph Simpson, device at NCM. Ft. Meade, MD
Notes: The Japanese wired the output plugboard identically to the input, even though they are independent. Apparently, the Japanese felt this was simpler and less error-prone for the user and the cryptologic strength of the plugboard is not as great as the key space implies. The US replica of Purple used one plugboard with wiring to go through it twice.
The decision to use 120 and later 240 start positions for the 20s stepping switches was made in order to reduce the number of messages sent in depth. The Japanese would disguise this practice by using additives. (see “Purple Revealed.” Freeman, Sullivan, Weierud. “Cryptologia” January, 2003, (Vol.26: No.1), p.18.

## Slide 36: Japanese Naval Code JN-25 Maximum Key Space
five-digit codes: = 105
five-digit additives: = 105
Maximum key space
1.00 x 1012
Example:
(100 word message) x
105 x 105 = 1012
Photo credit: Odacir Blanco via Wikimedia Commons
Photo credit: StationHypo.com

## Slide 37: Japanese Naval Code JN-25 Practical Key Space
30,000 five-digit additives
Practical key space
8.25 x 1010
Example:
(100 word message) x
27,500 x 30,000
27,500 five-digit codes
Photo credit: Odacir Blanco via Wikimedia Commons
Photo credit: StationHypo.com

## Slide 38: Lorenz SZ- 40/42 Key Space
# pins: 41,31,29,26,23
Pin setting: 2150
Start position:(pins)=2.20x107
5 Chi rotors:
# pins: 43,47,51,53,59
Pin setting: 2253
Start position: x(pins)=
3.22x108
5 Psi rotors:
# pins: 37,61
Pin setting: 298
Start position: 37x61=2257
2 Mu rotors:
2501 x (pins positions) =
2501 x (1.60x1019) =
Maximum & Practical key space
1.05 x 10170
Photo credit: Ted Coles, at The National Museum of Computing on Bletchley Park

## Slide 39: SG-41 “Hitler Mill” Key Space
# pins: 25,25,23,23,24,24
Pin setting: 2144
= 2.23x1043
Start position: 252x232x242
= 1.90x108
6 Rotors:
25 bars: lugs are fixed
= 1
Lugs:
Maximum & Practical key space
4.24 x 1051
Photo credit: Klaus Kopacz

## Slide 40: M-209 Maximum Key Space
Maximum key space
6.16 x 1060
Pin setting: 2131
= 2.72x1039
Start position:
26x25x23x21x19x17
= 101,405,850
(22 lug settings & 27 bars)
C(n+k-1,k)*= (n+k-1)!/(n-1)!k!
C(48,27) = (48!)/(21! x 27!)
= 2.23x1013
Lug Settings:
6 Rotors
*
“Stars and Bars” formula
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 41: M-209 Practical Key Space
Practical key space
6.02 x 1058
With US Army Constraints of 1942 = 2.18x1011
Pin setting: 2131
= 2.72x1039
Start position:
26x25x23x21x19x17
= 101,405,850
6 Rotors
Lug Settings:
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 42: Enigma M4 Maximum Key Space
Wiring: 26!
Order: 1
Start position: 26
Plugboard 0-13 plugs:
5.33x1014
Wiring: (26!)3
Order: 1
Notch (single or dual):
[(26)+(26x25)]2 = 264
Start position: 263
Maximum key space
2.33 x 10145
3 Rotors:
Thin Rotor:
Reflector:
(2p-1)(2p-3)…1 =
7.91x1012
Photo credit: Invaluable Auctions

## Slide 43: Enigma M4 Practical Key Space
Wiring: 1
Order: 2
Start position: 26
Plugboard 10 plugs:
1.51x1014
Wiring: 13
Order: 8x7x6 = 336
Notch setting: 262
Start position: 263
Practical key space
3.13 x 1025
3 Rotors of 8:
1 Thin Rotor of 2:
Reflector:
Fixed: 1
Photo credit: Invaluable Auctions

## Slide 44: Key Spaces of Historic Cipher Machines
Maximum Key Space
Practical Key Space
Cipher
Year
2.02x1053
1.60x10101
1.30x10532
7.17x10121
3.28x10114
1.82x10285
3.81x1059
1.00x1012
1.05x10170
4.24x1051
6.16x1060
2.33x10145
1.78x1029
1.85x109
2.43x1024
4.82x1010
4.31x1022
5.95x1028
1.45x1031
8.25x1010
1.05x10170
4.24x1051
6.02x1058
3.13x1025
Kryha
Enigma Swiss K
Lugagne Le Sphinx Strip Cipher
Abwehr Enigma G
Enigma I
SIGABA
Japanese Purple
Japanese JN-25 Code (100 words)
Lorenz SZ-40/42
SG-41 “Hitler Mill”
M-209 Pin & Lug
Enigma M4
2177
2336
21768
2405
2380
2941
2198
240
2565
2171
2202
2483
297
231
281
235
275
296
2104
236
2565
2171
2195
285
1924
1926
1930
1931
1932
1937
1939
1939
1941
1941
1942
1942
Copyright © 2023 ( CC BY 4.0 ) CipherHistory.com

## Slide 45: T-52d Geheimschreiber Maximum Key Space
Maximum key space
7.23 x 10213
Wiring: 2629 = 2.23x10189
Stepping: 1
Start position: (47x53x59x
61x64x65x67x69x71x73)
= 8.94X1017
Rotor plugboard switch:
10 rotors order: 10! =
3,628,800
10 rotors: 47,53,59,61,64,
65,67,69,71,73:
Photo credit: Reidar Olsen, Norway
Notes: 3 Rotating rotors:
    Notch setting can theoretically include notches on any of the 26 letters, or 2^26 for each rotor. Only notches on the 2nd and 3rd rotors from the left affect the rotor movements to the rotors to the left of them, just like the Enigma.
    Start position is not needed for solving one message, but the start position is needed to solve the “message key” to solve all messages from a single day (messages using the same internal settings).
2 Static rotors:
    Wiring for 2 rotors is only 26! Instead of (26!)^2 because the 2 rotors are stationary, so their wiring can be combined and considered as one rotor.
Entry disk and reflector are hard-wired in the machine, so is known by the enemy.
The entry disk plugboard can be plugged non-reciprocally, so A can be plugged to B and B can be plugged to C. The reflector plugboard is reciprocal, so if A is plugged to B, then B must be plugged to A.

## Slide 46: T-52d Geheimschreiber Practical Key Space
Practical key space
8.11 x 1023
10 rotors: 47,53,59,61,64,
65,67,69,71,73:
Wiring: 1
Stepping: 1
Start position: (47x53x59x
61x64x65x67x69x71x73)
= 8.94X1017
Rotor plugboard switch:
Σ rotors: 10!/5! = 30,240
π rotors: 30 (“Pentagon” logic)
Photo credit: Reidar Olsen, Norway
Notes: 3 Rotating rotors:
    Notch setting can theoretically include notches on any of the 26 letters, or 2^26 for each rotor. Only notches on the 2nd and 3rd rotors from the left affect the rotor movements to the rotors to the left of them, just like the Enigma.
    Start position is not needed for solving one message, but the start position is needed to solve the “message key” to solve all messages from a single day (messages using the same internal settings).
2 Static rotors:
    Wiring for 2 rotors is only 26! Instead of (26!)^2 because the 2 rotors are stationary, so their wiring can be combined and considered as one rotor.
Entry disk and reflector are hard-wired in the machine, so is known by the enemy.
The entry disk plugboard can be plugged non-reciprocally, so A can be plugged to B and B can be plugged to C. The reflector plugboard is reciprocal, so if A is plugged to B, then B must be plugged to A.

## Slide 47: Typex Mark 22 Maximum Key Space
Maximum key space
1.82 x 10195
Reciprocal =
7.91x1012
Reflector plugboard:
fixed: 1
Reflector:
Wiring: (26!)2
Order: 12
Side: 12
Notch setting: 12
Start position: 262
3 Rotating rotors:
Wiring: (26!)3
Order: 13
Side: 13
Notch setting: 226
Start position: 263
2 Static rotors of 8:
Entry disk plugboard:
fixed: 1
Entry
disk:
Non-reciprocal =
26! = 4.03x1026
Photo credit: Lawrence Wilkinson
Notes: 3 Rotating rotors:
    Notch setting can theoretically include notches on any of the 26 letters, or 2^26 for each rotor. Only notches on the 2nd and 3rd rotors from the left affect the rotor movements to the rotors to the left of them, just like the Enigma.
    Start position is not needed for solving one message, but the start position is needed to solve the “message key” to solve all messages from a single day (messages using the same internal settings).
2 Static rotors:
    Wiring for 2 rotors is only 26! Instead of (26!)^2 because the 2 rotors are stationary, so their wiring can be combined and considered as one rotor.
Entry disk and reflector are hard-wired in the machine, so is known by the enemy.
The entry disk plugboard can be plugged non-reciprocally, so A can be plugged to B and B can be plugged to C. The reflector plugboard is reciprocal, so if A is plugged to B, then B must be plugged to A.

## Slide 48: Typex Mark 22 Practical Key Space
Practical key space
5.51 x 1054
Wiring: 12
Order: 5x4 = 20
Side: 22
Notch setting: 12
Start position: 262
3 Rotating rotors:
Wiring: 13
Order: 8x7x6 = 336
Side: 23
Notch setting: 262
Start position: 263
2 Static rotors of 8:
Reflector plugboard:
fixed: 1
Entry disk plugboard:
Reflector:
fixed: 1
Entry
disk:
Reciprocal =
7.91x1012
Non-reciprocal =
26! = 4.03x1026
Photo credit: Lawrence Wilkinson
Notes: Total of 5 rotors used out of 8 available. The rotating and static rotors are interchangeable, so the order of 5 from 8 rotors is n!/(n-k)! = 8!/(8-5)! = 8x7x6x5x4=6720, which I divided as 336 for the rotating rotors and 20 for the static rotors. Equivalently, it could be 8x7=56 for the static rotors and 6x5x4=120 for the rotating rotors or any other combination of 8,7,6,5,4.

## Slide 49: NEMA Maximum Key Space
Reflector:
Entry rotor:
Wiring: fixed
Start position: 261
Maximum key space
5.99 x 10164
Notches: (226)4 = 2.03x1031
Order: 1
Start position: 264
Wiring: 26!4 = 2.65x10106
Order: 1
Start position: 264
4 Cipher rotors:
Wiring: 7.91x1012
Start position: 261
Stepping adjustment screws: 14
4 Stepping rotors:
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 50: NEMA Practical Key Space
Reflector:
Entry rotor:
Wiring: fixed
Start position: 261
Practical key space
1.83 x 1019
Notches: 14
Order: 6x5x4x3 = 360
Start position: 264
Wiring: 14
Order: 6x5x4x3 = 360
Start position: 264
4 Cipher rotors:
Wiring: 1
Start position: 261
Stepping adjustment screws: 14
4 Stepping rotors:
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 51: Hagelin C-52 Maximum Key Space
Maximum key space
1.68 x 10117
Pin setting: 238+41+42+43+46+47
= 2257 = 2.32x1077
Order: 12!/6! = 665,280
Start position: 38x41x42x
43x46x47 = 6.08x109
*
“Stars and Bars” formula
6 Rotors (25,26,29,31,34,37, 38,41,42,43,46,47):
Printer wheel offset: 26
Printer offset:
5 stepping bars have fixed teeth vs settable lugs, so # settings = 1
5 Stepping bars:
n=26 lug settings & k=27 bars
C(n+k-1,k) = (n+k-1)!/(n-1)!k!
C(90,27) = (90!)/(63! x 27!)
= 6.88x1022
27 Cipher bars:
*
Photo credit: Ralph Simpson, CipherHistory.com
Notes: # lug settings per bar:
6
∑ C(6,p) = 1+6+15+20+15+6+1 = 64
p=0

## Slide 52: Hagelin C-52 Practical Key Space
Practical key space
7.17 x 1057
Pin setting: 45-55% active
2121 - 299 = 2.66x1036
Order: 12!/6! = 665,280
Start position avg: (439/12)6 = 2.40x109
Printer wheel offset: 26
Printer offset:
n=26 lug settings & k=27 bars,
but Hagelin user manual recommendations provide only 65,000 lug settings
27 Cipher bars:
6 Rotors (25,26,29,31,34,37, 38,41,42,43,46,47):
Photo credit: Ralph Simpson, CipherHistory.com
5 stepping bars have fixed teeth vs settable lugs, so # settings = 1
5 Stepping bars:
Notes: Recommendations from the Hagelin manual, “The effect of computers on the security of Hagelin cryptographer type C-52”, No. R 7002 e, Oct. 1962.
Pin setting 6 Rotors from 25,26,29,31,34,37,38,41,42,43,46,47:
  Recommendation: 45-55% pins should be active
    Sum ( 25,26,29,31,34,37,38,41,42,43,46,47 ) / 2 = 439/2 = 219.5
    219.5 X 45% = 99
    219.5 X 55% = 121
    2^121 – 2^99 = 2.65x10^36
  Rotor start position: [Sum ( 25,26,29,31,34,37,38,41,42,43,46,47 ) / 12]^6
  = [439/12]^6
  = 2.40x10^9
Lug setting = 65,000

## Slide 53: Hagelin CX-52 Maximum Key Space
Maximum key space
1.17 x 10123
Pin setting: (247)6 =
2282 = 7.77x1084
Order: 1
Start position: 476 =
1.08x1010
6 47-pin rotors:
Printer wheel offset: 26
Printer offset:
27 Cipher bars:
n=26 lug settings & k=27 bars
C(n+k-1,k) = (n+k-1)!/(n-1)!k!
C(90,27) = (90!)/(63! x 27!)
= 6.88x1022
*
*
“Stars and Bars” formula
Rotor 1 always steps once 5 bars: 0-5 lug positions,
65 = 7,776
5 Stepping bars:
Photo credit: Ralph Simpson, CipherHistory.com
Notes: Pins setting:
40-60% active pins = 113-169 pins of 282
169
∑ C(282,p) = 282! / (282-p)! X p! =
p=113
113 –
114 –
115 –
5 stepping bar lug combinations
    N = 2^5 = 32, k=5
    C(36,5) = 36! / 31! X 5! = 376,992

## Slide 54: Hagelin CX-52 Practical Key Space
Practical key space
1.10 x 10104
Pin setting: 45-55% active
= (.55)(247)6 - (.45)(247)6
= 7.77x1083
Order: 1
Start position: 476
= 1.08x1010
6 47-pin rotors:
n=26 lug settings & k=27 bars, but Hagelin user manual recommendations provide only 65,000 lug settings
Printer wheel offset: 26
Printer offset:
Rotor 1 always steps once 5 bars: 0-5 lug positions,
65 = 7,776
5 Stepping bars:
27 Cipher bars:
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 55: KL-7 Maximum key space
Wiring: (36!)8
Order: 1
Start position: 368
Maximum key space
5.87 x 10431
8 Rotors:
Notches: (236)7
Order: 1
Start position: 367
7 Notch rings:
Photo credit: Navy-radio.com

## Slide 56: KL-7 Practical key space
Wiring: 17
Order: 11!/4!
= 1.66x106
Start position: 367
Practical key space
1.70 x 1034
7 Rotors from 11:
Notches: 17
Order: 11!/4!
= 1.66x106
Start position: 367
7 Notch rings from 11:
Static rotor:
Wiring: 1
Order: 1
Start position: 1
Photo credit: Navy-radio.com

## Slide 57: Transvertex HC-9 Maximum Key Space
16 Alphabets:
(5.33x1014) x 16 = 8.53x1015
Maximum key space
2.96 x 1071
Rotor start position:
265 = 11,881,376
Pin setting:
(2162) / 2 = (5.84x1048) / 2 =
2.92x1048
Photo credit: Ralph Simpson, CipherHistory.com
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 58: Transvertex HC-9 Practical Key Space
16 Alphabets:
Practical key space
4.39 x 1069
Rotor start position:
265 = 11,881,376
Pin setting:
(2162) / 2 = (5.84x1048) / 2 =
2.92x1048
User restriction: no letter encrypts to itself
(5.33x1014) x 16 = 8.53x1015
(7.91x1012) x 16 = 1.26x1014
Photo credit: Ralph Simpson, CipherHistory.com
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 59: Russian VIC Maximum Key Space
VIC Paper & Pencil cipher key:
Maximum key space
9.09 x 1040
Key Space =
105 x 1020 x 102 x (9.09x1013)
5 digit random key combined with
secret date = 105
2) 20 character secret phrase converted
to digits = 1020
3) 1 or 2 digit agent code = 102
10 chars. for straddling checkerboard
(a-z, 2 blanks, . , /) = 9.09x1013
Photo credit: FBI.gov
Photo credit: mysteriouswritings.com
Notes: Item 1) – A random 5 digit number and a secret date truncated to 5 digits seems like it should have a key space of 1010, but both numbers are combined into a single 5 digit number and the two original numbers are not used in the rest of the algorithm, so the key space is this combined 5 digit number = 105
Item 4) - The maximum key space for this, assuming the enemy knows the algorithm but not the changeable elements, means these 10 characters can be any letter, a-z plus the period, slash, and 2 blanks.
    Permutations of 10 items from (a-z, period, slash, two blanks)
    = P(30,10) = 30! / (30-10)! = 109,027,350,432,000 (but this includes 2 non-unique blanks)
    Permutations of 10 items from (a-z, period, slash, one blank)
    = P(29,10) = 29! / (29-10)! = 72,684,900,288,000
    Difference (Permutations with 2 blanks)
    = 36,342,450,144,000
    The Difference # has 2 blanks, but they could be interchanged, so the unique permutations with 2 blanks
    = 36,342,450,144,000 / 2
    Total = permutations allowing only one blank + permutations requiring two blanks
    = 72,684,900,288,000 + (36,342,450,144,000 / 2) = 90,856,125,360,000

## Slide 60: Russian VIC Practical Key Space
VIC Paper & Pencil cipher key:
Practical key space
1.00 x 1027
Key Space =
105 x 1020 x 102 x 1
5 digit random key combined with
secret date = 105
2) 20 character secret phrase converted
to digits = 1020
3) 1 or 2 digit agent code = 102
4) 10 chars. for straddling checkerboard,
(“snegopad” or snowfall, 2 blanks) = 1
Photo credit: FBI.gov
Photo credit: mysteriouswritings.com

## Slide 61: Hagelin CD-55 Maximum Key Space
TBD
Alphabet disk offset: 26
Alphabet offset:
Each disk has 1-16 steps but ≤32 total:
TBD
6 Displacement disks:
6 rotors (17,19,21,23,25,26 or
29,31,37,41,43,47) :
Pin setting:
Order: 1
Stepping: 1 (fixed)
Start position:
Notes: https://nsarchive.gwu.edu/document/19892-national-security-archive-18-correspondence (page 37)
Maximum displacement steps total = 32 (CD-57 allows up to 40 displacement steps)
17,19,21,23,25,26 or 29,31,37,41,43,47 – CD-55 (same as M-209 or CX-52a)
17,19,21,23,25,26 – C-446, M-209, C-38
29,31,37,41,43,47 – CX-52a
29,31,37,41,42,47 – CX-52b
25,26,34,38,42,46 - CX-52c
25,26,29,31,34,37,38,41,42,43,46,47 – C-52
,31,34,37,38,41,42,43,46,47 – CD-57
Choosing 6 of 12 disks – 12!/6! = 665,280
Pin settings – 2^(29+31+37+41+43+47) = 2^228
Displacement settings – using stars and bars formula:
C(n+k-1, k) = (n+k-1)! / (n-1)!k!
C(15+6-1,6) = 20! / 14! X 6! = 38,760
25,26,29(22 lug settings & 27 bars)
C(n+k-1,k)*= (n+k-1)!/(n-1)!k!
C(48,27) = (48!)/(21! x 27!)
= 2.23x1013

## Slide 62: FIALKA Maximum Key Space
Maximum key space
2.82 x 10458
10 Rotors:
Wiring: 30!10 =
1.72x10324
Order: 1
Side (1 or 2): 1
Rotation: 3010 =
5.90x1014
Start position:
3010 = 5.90x1014
Pin setting:
(230)8 = 1.77x1072
10 Wiring mazes:
Punched card:
30! = 2.65x1032
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 63: FIALKA Practical Key Space
Photo credit: Ralph Simpson, CipherHistory.com
Practical key space
6.24 x 1077
10 Rotors:
Punched card:
30! = 2.65x1032
Wiring: 1
Order: 10! =
3.63x106
Side: 210 = 1024
Rotation: 3010 =
5.90x1014
Start position:
3010 = 5.90x1014
Pin setting:
10!/2 = 1.81x106
10 Wiring mazes:

## Slide 64
Hagelin CD-57 Maximum Key Space
Maximum key space
1.52 x 10103
Alphabet disk offset: 26
Alphabet offset:
Each disk has 1-16 steps but ≤40 total:
(166)[(40) / (6x16)]
= 6.99x106
6 Displacement disks:
Photo credit: Rama via Wikimedia Commons
6 47-pin rotors:
Pin setting: (247)6 =
2282 = 7.77x1084
Order: 1
Stepping: 1 (fixed)
Start position: 476 = 1.08x1010
Notes: Hagelin technical manual, “Pocket Cryptographer Type CD-57, Technical Description, No. 3088 B” says CD-57 is the same cryptologically as the C-52 (not CX-52), but all 6 rotors only move one space at a time and each rotor can only cause the print wheel to advance up to 16 positions, at most, and 40 positions total for all 6 rotors.
    Basic keys
            Arrangement of stops on displacement disk:
            6 disks with lug settings = 1-16 each means 6 to 96 total steps are possible, but only 40 allowed
            So 6-40 steps out of (6-96) possible steps are allowed = 40/96
            Number of lug settings for displacement disks = 166 x (40/96) = 6,990,507 settings
            Choice of key wheels, assume 12 standard wheels: 25,26,29,31,34,37,38,41,42,43,46,47:
            Order of the 6 wheels from 12 = 12!/6! = 665,280
            Stepping = 1 because all rotors always step one position
            Arrangement of pins: Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = 439 total pins, so 2439/2 = 2219.5
            Recommendation: 1) 40-60% active pins: 60%(219.5) = 132 to 40%(219.5) = 88, so 2132 - 288 = 5.44x1039
            2) no more than 5 active/inactive in a row: reduction of 2 out of 64 settings for each pin
            position = [(64-2)/64]^219.5 valid pin settings = 9.07x10^-4
            result = 1) x 2) = 5.12x1036
- Position of alphabet ring = 26
    Initial keys
- Start position of key wheels = Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = (439/12)6 = 2.40x109

## Slide 65
Hagelin CD-57 Practical Key Space
Pins: 1) 40-60% active = 2(439/2)(.6) – 2(439/2)(.4)
= 2132 - 288 = 5.44x1039
2) <6 active/inactive pins in row,
[(26 - 2) / 26]439/2 = 9.41x10-4
= 1) x 2) = 5.12x1036
Order: 12!/6! = 665,280
Stepping: 1 (fixed)
Start position: (439/12)6 = 2.40x109
6 Rotors (25,26,29,31,34,37,38,41,42,43,46,47):
Practical key space
1.49 x 1060
Alphabet disk offset: 26
Alphabet offset:
Each disk has 1-16 steps but ≤40 total:
(166)[(40) / (6x16)]
= 6.99x106
6 Displacement disks:
Photo credit: Rama via Wikimedia Commons
Notes: Hagelin technical manual, “Pocket Cryptographer Type CD-57, Technical Description, No. 3088 B” says CD-57 is the same cryptologically as the C-52 (not CX-52), but all 6 rotors only move one space at a time and each rotor can only cause the print wheel to advance up to 16 positions, at most, and 40 positions total for all 6 rotors.
    Basic keys
            Arrangement of stops on displacement disk:
            6 disks with lug settings = 1-16 each means 6 to 96 total steps are possible, but only 40 allowed
            So 6-40 steps out of (6-96) possible steps are allowed = 40/96
            Number of lug settings for displacement disks = 166 x (40/96) = 6,990,507 settings
            Choice of key wheels, assume 12 standard wheels: 25,26,29,31,34,37,38,41,42,43,46,47:
            Order of the 6 wheels from 12 = 12!/6! = 665,280
            Stepping = 1 because all rotors always step one position
            Arrangement of pins: Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = 439 total pins, so 2439/2 = 2219.5
            Recommendation: 1) 40-60% active pins: 60%(219.5) = 132 to 40%(219.5) = 88, so 2132 - 288 = 5.44x1039
            2) no more than 5 active/inactive in a row: reduction of 2 out of 64 settings for each pin
            position = [(64-2)/64]^219.5 valid pin settings = 9.07x10^-4
            result = 1) x 2) = 5.12x1036
- Position of alphabet ring = 26
    Initial keys
- Start position of key wheels = Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = (439/12)6 = 2.40x109

## Slide 66
Hagelin HX-63 Maximum Key Space
Maximum key space
1.49 x 10600
Alphabet disk offset: 26
Alphabet offset:
Starting position: 4141
9 Rotors of 12:
Photo credit: Peter Adams
Wiring: (41!)9
Order: 12! / (12-9)!
= 79,833,600
Notches:
Starting position: 419
Rotary stepping switch:
Entry Rotor:
Wiring: 1
Non-reciprocal:
41!
Reflector:
Notes: Hagelin technical manual, “Pocket Cryptographer Type CD-57, Technical Description, No. 3088 B” says CD-57 is the same cryptologically as the C-52 (not CX-52), but all 6 rotors only move one space at a time and each rotor can only cause the print wheel to advance up to 16 positions, at most, and 40 positions total for all 6 rotors.
    Basic keys
            Arrangement of stops on displacement disk:
            6 disks with lug settings = 1-16 each means 6 to 96 total steps are possible, but only 40 allowed
            So 6-40 steps out of (6-96) possible steps are allowed = 40/96
            Number of lug settings for displacement disks = 166 x (40/96) = 6,990,507 settings
            Choice of key wheels, assume 12 standard wheels: 25,26,29,31,34,37,38,41,42,43,46,47:
            Order of the 6 wheels from 12 = 12!/6! = 665,280
            Stepping = 1 because all rotors always step one position
            Arrangement of pins: Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = 439 total pins, so 2439/2 = 2219.5
            Recommendation: 1) 40-60% active pins: 60%(219.5) = 132 to 40%(219.5) = 88, so 2132 - 288 = 5.44x1039
            2) no more than 5 active/inactive in a row: reduction of 2 out of 64 settings for each pin
            position = [(64-2)/64]^219.5 valid pin settings = 9.07x10^-4
            result = 1) x 2) = 5.12x1036
- Position of alphabet ring = 26
    Initial keys
- Start position of key wheels = Ʃ 25,26,29,31,34,37,38,41,42,43,46,47 = (439/12)6 = 2.40x109

## Slide 67: RSA-4096 Key Space
Key = product of 2 primes, (pxq), where 22047.5 < p < q < 22048
Key space = total number of unique prime pairs: p and q
22047
20
22048
22047.5
Maximum & Practical key space
2.22 x 101225
Calculation of key space = (# primes)2 / 2
(note1: divide by 2 because pxq = qxp)
(note2: (# primes ≤ n) = π(n) ≈ n / ln(n) )
= [ π(22048) - π(22047.5 ) ]2 / 2
= [ (22048 / ln(22048) ) - (22047.5 / ln(22047.5 ) ) ]2 / 2
= [ 2.27654x10613 - 1.61015x10613 ]2 / 2
= 2.22x101225 ≡ 24070.51

## Slide 68: AT&T TSD 3600-E “Clipper Chip” Key Space
Clipper Chip designed with advertised front door access
Clipper Chip has proprietary NSA Skipjack encryption program
Skipjack similar to DES, but with an 80 bit key: key space = 280
Maximum & Practical key space
1.21 x 1024
Photo credit: Ralph Simpson, CipherHistory.com
Photo credit: Ralph Simpson, CipherHistory.com

## Slide 69: Key Spaces of Historic Cipher Machines
7.23x10213
1.82x10195
5.99x10164
1.68x10117
1.17x10123
5.87x10431
2.96x1071
9.09x1040
TBD
2.82x10458
1.52x10103
7.21x1016
2.22x101225
1.21x1024
1.16x1077
8.11x1023
5.51x1054
1.83x1019
7.17x1057
1.10x10104
1.70x1034
4.39x1069
1.00x1027
TBD
6.24x1077
1.49x1060
7.21x1016
2.22x101225
1.21x1024
1.16x1077
T-52d Geheimschreiber
Typex Mark 22
NEMA
Hagelin C-52
Hagelin CX-52
KL-7
Transvertex HC-9
VIC Paper & Pencil
Hagelin CD-55
Fialka
Hagelin CD-57
DES (56 bit)
RSA-4096
AT&T TSD 3600-E Clipper Chip
AES-256
2710
2649
2551
2389
2409
21434
2237
2136
21523
2343
256
24071
280
2256
279
2182
264
2192
2346
2114
2231
290
2258
2200
256
24071
280
2256
1942
1943
1947
1952
1952
1952
1950s
1953
1955
1956
1957
1976
1977
1992
2001
Maximum Key Space
Practical Key Space
Cipher
Year
Copyright © 2023 ( CC BY 4.0 ) CipherHistory.com

## Slide 70: Key Spaces of Historic Cipher Machines
4.03x1026
2.50x101
1.68x1021
2.00x10444
6.20x1023
4.03x1026
1.30x10532
3.45x10666
3.69x10799
4.19x1047
1.01x1064
1.27x10140
2.02x1053
1.60x10101
1.30x10532
7.17x10121
3.28x10114
1.82x10285
3.81x1059
1.00x1012
1.05x10170
4.24x1051
6.16x1060
2.33x10145
7.23x10213
1.82x10195
5.99x10164
1.68x10117
1.17x10123
5.87x10431
2.96x1071
9.09x1040
2.82x10458
1.52x10103
7.21x1016
2.22x101225
1.21x1024
1.16x1077
4.03x1026
2.50x101
1.68x1021
2.00x10444
6.20x1023
4.03x1026
1.32x1013
3.88x1026
1.95x1059
4.19x1047
1.01x1064
4.56x1010
1.78x1029
1.85x109
2.43x1024
4.82x1010
4.31x1022
5.95x1028
1.45x1031
8.25x1010
1.05x10170
4.24x1051
6.02x1058
3.13x1025
8.11x1023
5.51x1054
1.83x1019
7.17x1057
1.10x10104
1.70x1034
4.39x1069
1.00x1027
6.24x1077
1.49x1060
7.21x1016
2.22x101225
1.21x1024
1.16x1077
Maximum Key Space
Practical Key Space
Monoalphabetic
Caesar
Vigenère (repeating keyword - 15 char.)
Vigenère (autokey - 314 char. message)
Playfair
Wheatstone Cryptograph
Lugagne Transpositeur
M-94 Cylinder Cipher
M-138A Strip Cipher
ADFGX
ADFGVX
Hebern 5-Rotor
Kryha
Enigma Swiss K
Lugagne Le Sphinx
Abwehr Enigma G
Enigma I
SIGABA
Japanese Purple
Japanese JN-25 Codebook (100 words)
Lorenz SZ-40/42
SG-41 “Hitler Mill”
M-209 Pin & Lug
Enigma M4
T-52d Geheimschreiber
Typex Mark 22
NEMA
Hagelin C-52
Hagelin CX-52
KL-7
Transvertex HC-9
VIC Paper & Pencil
Fialka
Hagelin CD-57
DES (56 bit)
RSA-4096
AT&T TSD 3600-E Clipper Chip
AES-256
288
25
271
21476
279
288
21768
22214
22656
2158
2213
2466
2177
2336
21768
2405
2380
2941
2198
240
2565
2171
2202
2483
2710
2649
2551
2389
2409
21434
2237
2136
21523
2343
256
24071
280
2256
288
25
271
21476
279
288
244
288
2197
2158
2213
235
297
231
281
235
275
296
2104
236
2565
2171
2195
285
279
2182
264
2192
2346
2114
2231
290
2258
2200
256
24071
280
2256
600 BCE
50 BCE
1466
1586
1854
1860s
1912
1912
1916
1918
1918
1922
1924
1926
1930
1931
1932
1937
1939
1939
1941
1941
1942
1942
1942
1943
1947
1952
1952
1952
1950s
1953
1956
1957
1976
1977
1992
2001
Cipher
Year
Copyright © 2023
( CC BY 4.0 )
CipherHistory.com

## Slide 71
Download this presentation
CipherHistory.com / keyspaces
Cipher History Museum

## Slide 72
Word Crunching
by Bill Bilston
I
wrote
a poem
on a page
but then each line grew
to the word sum of the previous two
until I began to worry about all these words coming with such frequency
because as you can see, it can be easy to run out of space when a poem gets all fibonacci sequency
I could have happily ended this small poem with the words above
because it was increasingly difficult to write each additional line
so in my struggle to add another couplet, the problem loomed cataclysmic
but then I found a solution to my space problem by something called word wrap
and also found solace in the fact I was set free to express myself
without the creative limitation of just a few words on a line
but still I am glad the sequence I chose was Fibonacci and not logarithmic

## Slide 73
Word Crunching
I
wrote
a poem
on a page
but then each line grew
to the word sum of the previous two
until I began to worry about all these words coming with such frequency
because as you can see, it can be easy to run out of space when a poem gets all fibonacci sequency
I could have happily ended this small poem with the words above
because it was becoming a struggle to write each additional line
and by trying to add another couplet, the problem seemed existential
but then I found a solution to the space problem by a technique called word wrap
and also found solace in the fact I was much more free to express myself
without the limitation of a few words on a line
but still I am glad the sequence I chose was Fibonacci and not exponential